## Slide 1: AIRPORT OPERATIONS MANAGEMENT ASSISTANCE PROJECT
RECO
Filippo MONTANARI
2019/2020
Michelle BONATI

## Slide 2: PROBLEM 1
SCHEDULING OF CHEK-IN AGENTS
1
The first management problem concerns the scheduling of check-in agents for an airline, to ensure a minimum number of agents at a minimum cost.

## Slide 3: DAILY PLANNING
Problem
Find the daily number of agents so as to ensure the minimum required service and the minimum cost.
Daily service: 8h
Extra service: 4h
Cost extra service = 150% cost of regular service
Solution
Excel Solver, minimization - Simplex
The objective function is the total cost:
The variables are the numbers of agents starting each turn in case of both normal time and extra time.
The constraints are:
1
A

## Slide 4: LIMITATION OF WORK OVERTIME
Problem
Find the daily number of agents so as to ensure the minimum required service and the minimum cost. Each agent can perform extra service no more than once every 3 days.
Solution
Excel Solver, same procedure as problem A
The objective function is the total cost:
The variables are the number of agents starting each turn in case of both normal time and extra time.
The constraints are:
Additional constraints
as integer numbers
as integer numbers
1
B

## Slide 5: WEEKLY SIZING
Problem
Find the weekly number of agents so as to ensure the minimum required service and the minimum cost.
Solution
Excel Solver, minimization - Simplex
The objective function is the total cost, which is equal to the number of agents per week.
The variables are the number of agents starting at each day of the week.
The constraint are:
as integer numbers
1
C

## Slide 6: PROBLEM 2
ASSIGNMENT OF CREWS TO FLIGHTS
2
The second problem can be divided into two tasks:
Finding all the possible flight sequences
Finding the flight sequences to adopt in order to minimize the cost of the crews.
These two tasks are part of the Crew Pairing problem.

## Slide 7: PROBLEM 2 – USER INTERFACE
1
2
3
4
2

## Slide 8: CREW PAIRING – GANTT CHART OF THE FLIGHTS
Problem
Display flights as a function of hours in the GANTT chart given the flights schedule.
Solution
Visual Basic code
For each flight
For each time cell of the Gantt
If [the time on the GANTT chart is later or equal to the departure time in the input table] And [the time on the GANTT chart is earlier than the arrival time in the input table] Then
Mark the Gantt cell
End If
Next
Next
2
A

## Slide 9: CREW PAIRING – ADJACENCY MATRIX
2
B
Problem
Find the algorithm of constitution of the adjacency matrix of the flight graph according to the flight table.
Conditions:
Each consequent flight will have the same departure airport as the arrival airport of the previous flight.
Each flight will depart later than the previous flight’s arrival.
Solution
Visual Basic code
For each flight i, search a pair j
If [the pairing flight j is different from flight i] And [the departure airport of flight j is equal to the arrival airport of the flight i] And [the departure time of the flight j is later than the arrival time of flight i] Then
Write 1 into the cell
End if
Next

## Slide 10: CREW PAIRING – FLIGHT SEQUENCES
2
C
Problem
Enumerate all the possible flight sequences (starting from the adjacency matrix).
Solution
This is a Depth-first search problem (‘parcours en profondeur’)
Visual Basic code
For each line of the adjacency matrix
If a non-closed path can be found Then
While Not a closed cell is reached
Follow the path in depth and write the sequence
Wend
Close the explored path by marking the last explored cell
End if
Next
More in the attachment…

## Slide 11: CREW PAIRING – FLIGHT SEQUENCES
2
D
Problem
Temporal graphical representation of possible flight sequences.
Solution
Visual Basic code
Refer to the sequence table
For each sequence
While there are flights in the sequence
Search for the flight data in the input table and insert it in the Gantt diagram, associating a different color to each different flight.
Wend
Next
More in the attachment…

## Slide 12: CREW PAIRING – RECOVERY PROBLEM
2
E
Problem
Optimization problem, posed as a recovery problem. We aim at minimizing the cost of the crews.
k index of the sequence
=1 if at least one crew is assigned to the sequence k
=0 otherwise
Solution
Excel solver, minimization - Simplex
The objective function is the minimum cost Z:
The variables are , where goes from 1 to the number of sequences
Constraints for each flight i:

## Slide 13: CREW PAIRING – RESULTS
2
F
Once launched the app, a VBA code allows to run all its consequent parts shown in the slides before.
Finally, the crews and the assigned flights are shown in the results table.

## Slide 14: PROBLEM 3
GROUND OPERATIONS MANAGEMENT - PASSENGER TRANSPORT
3
The third problem consists in optimizing the management of the bus fleet that allows the passengers transportation from the terminal to their aircraft and vice versa.

## Slide 15: PROBLEM 3 – USER INTERFACE
3
1
3
2
5
4

## Slide 16: PASSENGER TRANSPORT
3
A
Problem
Establish a linear programming model to optimize the management of the bus fleet.
Passengers have to be transported from the terminal to their aircraft or vice versa.
Find the order in which the bus should visit the planes/terminal so as to minimize the total delay of all the operations.
This can be seen as a Schedule Problem 1|ri|T, in which 1 machine (the bus) must perform 6 tasks (visiting the plane/terminals/deposit) respecting availability time constraints ri and minimizing the delay T.
Solver’s input tables

## Slide 17: PASSENGER TRANSPORT
3
B
Solution
Excel Solver, minimization - Simplex
The objective function is the minimum total distance flown
Min Z = Σi(penality*delay)+Σi(penality distance*distance)
The variable is the actual time of transport Y
Constraints:
If the bus passes from i to j, then the arrival hour to j must be greater or equal to the arrival hour to i + the time required to board/unboard + the time required to reach j starting from i:
The arrival hour of the bus to i must be greater or equal to the hour in which the passengers are ready to board /unboard:
Only one stop to each plane/terminal:
Solver’s variables and constraints

## Slide 18: PASSENGER TRANSPORT
3
C
Results
The results table returns to the user :
the arrival time to each plane/terminal
If the flight is late
The delays
A graphical sequence of the path that the bus should follow to minimize the total delay

## Slide 19: PROBLEM 4
ASSIGNMENT OF FLIGHTS
TO BOARDING GATES
4
The objective is to assign each flight to an available gate, according to an estimated time window, so as to minimize the number of flights waiting on the apron.

## Slide 20: ASSIGNMENT OF FLIGHTS AT BOARDING GATES – OPTIMIZATION PROBLEM
4
Constraints of the optimization problem
For reasons of space and fluency, we decided to not add the comments about the constraints of the optimization problem in this presentation.
They can be read in the attached text document.

## Slide 21: PROBLEM 4 – USER INTERFACE
4
1
2
3

## Slide 22: ASSIGNMENT OF FLIGHTS AT BOARDING GATES - INPUT TABLE
4
A
Added in real
time by the user
When the actual arrival time of a plane is known, the user can add it to the table and, if the auto-update option is enabled, the app will automatically update the results.
auto-update option
<Oui, Non>

## Slide 23: ASSIGNEMENT OF FLIGHTS AT BOARDING GATES – GANTT OF THE FLIGHTS
4
B
Problem
Trace the GANTT chart of the flights, including the estimated time window and, when available, the real time window.
Solution
Visual Basic code
For each flight
Trace the estimated time window inside the Gantt
If the actual arrival time exists Then
Trace the real time window inside the Gantt
If a portion of the real window passes the estimated time window Then
Trace that portion in red
End If
End if
Next

## Slide 24: ASSIGNEMENT OF FLIGHTS AT BOARDING GATES – GANTT OF THE GATES
4
C
Problem
Trace the GANTT chart of the gates.
Assign each plane to a free gate by using the Greedy algorithm. If there are no free gates, assign the plane to the apron.
If the real arrival time is not available, then use the estimated time window. Otherwise, use the real time window.
Solution
Visual Basic code
For each flight
If the actual arrival time exists Then
Calculate the time window with arrival time and gate duration
Else : Consider the estimated time window
End If
For each gate
If [the gate is the one with the longest schedule] And [the time window of the flight starts later than the last moment in which the gate is occupied] Then
Trace the flight inside the gate line
End If
Next
If no suitable gate was found
Add the flight to the apron Then
End If
Next

## Slide 25: ASSIGNEMENT OF FLIGHTS AT BOARDING GATES – GANTT OF THE GATES
4
D
The app can update the GANTT charts in no more than 5 seconds
When a new entry is detected in the Arrival Time column, the app calculates a new and better solution for the problem.
As shown in the chart aside, the updated solution allocates to the apron a lowest number of flights.
Moreover, all the flights for which the arrival time is known are allocated to a gate.

## Slide 26: THANK YOU for your attention